## Slide 1: Referee Study on Germination of Canarygrass (Phalaris canariensis)
Lei Ren
2023 AOSA Annual Meeting
              June 14, 2022

## Slide 2: Objectives
To promote uniformity, standardization, and precision among seed laboratories.
To provide data to be used as supporting evidence harmonization of Canadian M&P, AOSA and ISTA rules.
To identify specific areas in the Canarygrass germination test in which investigation or research is needed.
Notes: To promote uniformity, standardization, and precision among seed laboratories with regard to the evaluation of temperatures equivalency specified in three sets of rules.
To provide data to be used as supporting evidence for future seed testing procedures and rule changes, such as harmonization of Canadian M&P, AOSA and ISTA seed testing procedures and rules.
To identify specific areas in the rapeseed germination test in which investigation or research is needed to promote uniform results among laboratories.

## Slide 3: Germination Rule Comparison
Testing Rules | Substrata | Temperatures (oC) | Counting days
M&P | BP, RT | 15-25 | 7 and 10
ISTA | BP, TP | 15-25; 20-30 | 7 and 21
AOSA | B, T | 20-30 | 3 and 7
Notes: We analyzed the rule difference and hypothesized that temperature and counting dates are the potential factors that could cause the difference of germination results

## Slide 4: Testing Method
Temperatures (oC) | Substrata | Seeds X Reps | Counting days
15-25 | BP/B* | 100 X 4 | 3, 7, 10, 14 and 21
20-30 | BP/B* | 100 X 4 | 3, 7, 10, 14 and 21
* BP substrata is following the M&P Rule; B substrata is following the AOSA Rule. Both are between blotters

## Slide 5: Pre-trial Within SSTS
Chart: Normal 20-30oC
| Lot1 | Lot2 | Lot3 | Lot4 | Lot5 | Lot6 | Lot7 | Lot8 | Lot9
Nomral | 93 | 88 | 97 | 74 | 94 | 82 | 86 | 81 | 93
Notes: Non dormant seeds for this test

## Slide 6: Referee study: Inter-Laboratory Study
Lot 2, 4 and 8
10 samples for homogeneity test
15-25oC
20-30oC
13.5 g (2000 seeds) 60 samples
28 samples
Mixing and dividing
Notes: Sample variation are randomly and evenly distributed in each temperature and participant when the homogeneity test is passed, therefore sample factor to all samples and participants are equivalent statistically.
3 seed lots, 60 samples were used in the referee study

## Slide 7: Participants
In total, there are 28 labs attending this referee study
  11 from Canada
  17 from USA
This presentation includes 27 labs data
  All 27 labs provided 15-25 oC data
  24 out of 27 labs provided 20-30 oC data
Final report will include 28 labs data

## Slide 8: Result: Source of Variation
ANOVA table |  | Normal Seedlings |  |  |  |  | AB seedlings | Ungerminated seeds
 |  | Day 3 | Day 7 | Day 10 | Day 14 | Day 21 |  | 
Source | DF | Pr > F | Pr > F | Pr > F | Pr > F | Pr > F | Pr > F | Pr > F
temperature | 1 | 0.0117 | 0.2346 | 0.816 | 0.6003 | 0.2843 | 0.378 | 0.0164
seedlot | 2 | 0.0443 | <.0001 | <.0001 | <.0001 | <.0001 | <.0001 | <.0001
temperature*seedlot | 2 | 0.1833 | 0.2956 | 0.0101 | 0.0288 | 0.0724 | 0.0005 | 0.8418
Notes: All data was analyzed by Glimmix Model using SAS 9.4
Sources of variation that impact the result (significant)
Fvalue – higher indicates more variation
Pr>F (p value) is significant less than 0.05 is significant
No significant different for Tem effect

## Slide 9: Germination of Each Seed Lot
Chart: Catogary
| Normal | Abnormal | Ungerminated seeds
Lot2 | 90.5552 | 2.175 | 7.2696
Lot4 | 76.9631 | 4.7565 | 18.2863
Lot8 | 85.3576 | 2.986 | 11.8022
In line with pre-trial results

## Slide 10: Result - Lab Variation

## Slide 11: Result - Lab Variation (Con.)
Lowest germination lot has the highest variation among lab testing

## Slide 12: Temperature Effect on Germination
No differences between the two tested temperatures
Chart: Catogary
| Normal | Abnormal | Ungerminated seeds
15-25C | 84.5401 | 3.463 | 12
20-30C | 84.0438 | 3.1488 | 12.9055
a
a
a
a
a
a
Notes: 20 C is consistent highest result and the least range.

## Slide 13: Normal Seedling Germ Trend
Chart: Germination %
| Day 3 | Day 7 | Day 10 | Day 14 | Day 21
Lot2 | 10 | 83 | 89 | 91 | 90.5552
Lot4 | 8.8472 | 67 | 72 | 76.4912 | 76.9631
Lot8 | 11.1988 | 77.0185 | 81.8758 | 84.9655 | 85.3576
Chart: Germination %
| Day 3 | Day 7 | Day 10 | Day 14 | Day 21
15-25C | 5.2006 | 74.1891 | 81.0679 | 84.0385 | 84.5401
20-30C | 15.2394 | 77.0389 | 80.9121 | 83.8096 | 84.0438
Notes: Same information. Visual representation of temperature difference. Same color bar mean not significantly different. It should be one color bar if the temps gave equivalent results.

## Slide 14: Counting Dates Effect on Germination
Chart: Normal seedlings
| Day3 | Day7 | Day10 | Day14 | Day21
 | 10.2783 | 76 | 81.147 | 83.7722 | 84.3267
c
b
ab
a
a

## Slide 15: Result: Lab performance rating
Result rating against mean
Mean
A
B
C
D
B
C
D
Z-score. The Z-score compares the distance of the participant’s result from the overall sample
mean, to the average difference from the mean of all participants. A Z-score of zero indicates the
participant’s result equaled the overall mean. A high number indicates the participant’s result
was far away from the mean.
Notes: a. Z-score. The Z-score compares the distance of the participant’s result from the overall sample
mean, to the average difference from the mean of all participants. A Z-score of zero indicates the
participant’s result equaled the overall mean. A high number indicates the participant’s result
was far away from the mean. Evaluated the same way we would do a PT. Sum of z score over 3 lots.

## Slide 16: Lab performance
Testing uniformity are variable in different temperatures
Chart: 
| A | B | C
15-25°C | 0.81481 | 0.074074 | 0.11111
Chart: 
| A | B | C
20-30°C | 0.79167 | 0.16667 | 0.041667
Notes: Category standards used for performance evaluation
Σ absolute
z- Score
Performance
rating
Feedback Action Suggestions
0.00 – 3.49 A Acceptable, no action needed.
3.50- 5.29 B Review of methods is recommended.
5.30 – 6.99 C Lab should investigate possible problem
> 6.99 D Lab should investigate possible problem. It is Below
Minimum Performance of expected as Canadian or ISTA
accredited laboratory

## Slide 17: Discussion
Lab is a large variable influencing testing uniformity. Lab variation is larger for the seed lot with lower germination.
  Training?
  Proficiency monitoring?
  Clarities in rules or assistance on seedling evaluation?
Two tested temperatures did not have significant effects on germination % in this referee study.
Suggested counting dates vary among the three rules
  Is 7 day counting long enough to capture the final germination?
  Is 21 day counting needed?
  10 or 14 day counting is good enough?
  A method validation study needed?

## Slide 18: Validation Study Plan
Follow ISTA validation process:
Participants:
  ISTA accredited labs in U.S., Canada, others who are interested in
  AOSA lab and Canadian labs
Experience: experienced labs
Seed lots: 6 seed lots with a wider germination range from 75-95%

## Slide 19: Acknowledgement
Germination group
Jo Ann Hornseth
Maria Cumming
Nicole Wurm
Research group
Julie Lu
Ruojing Wang

## Slide 20: Questions?